## Slide 1: Reconstructing Audio From Video
Rishi Kapadia
Baladitya Yellapragada
CS 294-127 Final Project

## Slide 2: Motivation
Based on Eulerian Video Magnification framework by the CSAIL research group at MIT
Notes: Our original idea was to use a high-speed camera to recover speech audio from a video of someone’s throat while they are talking. To start off, and to ensure more consistency between experiments, we decided to videotape a base speaker as it is playing music.

## Slide 3: Eulerian Video Magnification
http://people.csail.mit.edu/mrub/vidmag/
Notes: Here is some background into the series of papers on Eulerian Video Magnification. They attempted to decompose a high-speed video both temporally and spatially, filter each pixel in the decomposed video temporally to capture a certain range of frequencies, and then add that filtered signal times alpha back to the original decomposition, and collapse the decomposition into an amplified video.

## Slide 4: Amplifying Color Variations
http://people.csail.mit.edu/mrub/vidmag/
Notes: Here is one result of amplifying color variations using that technique.

## Slide 5: Motion Magnification
http://people.csail.mit.edu/mrub/vidmag/
Notes: Here is another example where they use different cutoff frequencies in their temporal filters to amplify spatial motions for certain frequencies, namely the first and then the second strings of the guitar, respectively.

## Slide 6: Audio Reconstruction
http://www.niemanlab.org/images/jeffjarvisvideo.png
Notes: Since we want to reconstruct the audio signal only, and not amplify and display the variations in the original video, we do not need to do a spatial decomposition of our input video. Instead, we propose to take a high speed video of someone’s throat while they are talking, look at the pixel with the largest amplitude difference, and then filter that 1D signal over time to recover the audio of the person speaking. We realize that just looking at the throat alone may not convey syllables, which would require also looking at the embouchure of the tongue and mouth, but we at least wanted to see if we can recover the pitch of the voice. This is different from the Visual Microphone experiment conducted by CSAIL because we are analyzing a video of an audio source, instead of an indirect, malleable, or passive object in the environment.

## Slide 7: Experimental Setup
Camera we used
Bass speaker
LED flashlights from our mobile phones
  Get rid of flickering from fluorescent lights
Audacity to generate audio clips of single and multiple frequencies

## Slide 8: 1D Camera Output
50 Hz Audio Signal

## Slide 9
Problems we had along the way
Focus issues, with a 1D camera
  1D camera not very sensitive to higher frequency oscillations, due to lack of focus
Lighting changes
  Fluorescent lights had an oscillating signal by itself
  Natural light had no oscillations, but sunlight intensity changes frequently

## Slide 10: Reconstructions
Input audio to base speaker, 1 frame of video output, FFT of signal reconstruction, audio reconstruction
Single frequency reconstructions
Double frequency recs
Skrillex/music rec
Human voice/throat rec (failed)
Maybe SNR, or other numbers? Some sort of table

## Slide 11
Summary, conclusion, takeaways
Things we would have done differently